## Slide 1: Creating Multi-Threaded Programs and Controllers
James Edmondson
Notes: Title Slide
  Title and Subtitle text blocks should not be moved from their position if at all possible.

## Slide 2
Copyright 2016 Carnegie Mellon University This material is based upon work funded and supported by the Department of Defense under Contract No. FA8721-05-C-0003 with Carnegie Mellon University for the operation of the Software Engineering Institute, a federally funded research and development center. Any opinions, findings and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the United States Department of Defense. NO WARRANTY. THIS CARNEGIE MELLON UNIVERSITY AND SOFTWARE ENGINEERING INSTITUTE MATERIAL IS FURNISHED ON AN “AS-IS” BASIS. CARNEGIE MELLON UNIVERSITY MAKES NO WARRANTIES OF ANY KIND, EITHER EXPRESSED OR IMPLIED, AS TO ANY MATTER INCLUDING, BUT NOT LIMITED TO, WARRANTY OF FITNESS FOR PURPOSE OR MERCHANTABILITY, EXCLUSIVITY, OR RESULTS OBTAINED FROM USE OF THE MATERIAL. CARNEGIE MELLON UNIVERSITY DOES NOT MAKE ANY WARRANTY OF ANY KIND WITH RESPECT TO FREEDOM FROM PATENT, TRADEMARK, OR COPYRIGHT INFRINGEMENT. [Distribution Statement A] This material has been approved for public release and unlimited distribution. Please see Copyright notice for non-US Government use and distribution. This material may be reproduced in its entirety, without modification, and freely distributed in written or electronic form without requesting formal permission. Permission is required for any other use. Requests for permission should be directed to the Software Engineering Institute at permission@sei.cmu.edu. Carnegie Mellon® is registered in the U.S. Patent and Trademark Office by Carnegie Mellon University. DM-0003735

## Slide 3
In this talk, we will discuss the creation of multi-threaded programs and controllers using the GAMS and MADARA projects
Introduction
Generation
Notes
Next Steps
  In this talk, we will learn
    What a multi-threaded program is
    How to create a multi-threaded program
    How to use thread-safe MADARA features
    How to integrate multi-threaded programs with GAMS controllers
    How to network multi-threaded programs together
Thread Safety
Example App

## Slide 4
What is a multi-threaded program?
program
thread1
thread2
A multi-threaded program is a process that spawns multiple threads of execution, generally to accomplish objectives in parallel
thread2
Multi-threaded programs tend to be more persistent as operating system resources are required to create and maintain threads
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 5
Why is writing multi-threaded programs difficult?
program
thread1
thread2
The primary problems for developers of multi-threaded programs are race conditions
thread2
A race condition is a catch-all term for unexpected issues with synchronization and memory caching within multi-threaded and some multi-processed applications
Dealing with race conditions requires access to thread-safe primitives and can aided by scheduling threads in predictable execution paths
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 6
The GAMS Project Configurator (GPC) is useful for generating MADARA and GAMS features for developers to start with, including threads
New threads can be created with the --new-thread or --nt argument
gpc.pl
project
controller
threads
  $GAMS_ROOT/scripts/projects/gpc.pl --path $PROJECT_ROOT/tutorial2 --new-thread sensor --nt analyzer --nt planner
Linux terminal
  %GAMS_ROOT%\scripts\projects\gpc.pl --path %PROJECT_ROOT%\tutorial2 --new-thread sensor --nt analyzer --nt planner
Windows: Open Visual Studio Developer Command Prompt (Start->All programs->Visual Studio 20XX->Visual Studio Tools->Developer Command Prompt)
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 7
Understanding what is generated by --new-thread
  The new thread option creates a .h and .cpp file in src/threads
    Header and source files are filled in with minimal implementations
    The files are never overwritten, and developers are encouraged to edit them
  The --new-thread option also creates or modifies src/controller.cpp
    A MADARA Threader object controls the creation and management of threads
    Developers can edit the controller.cpp file to affect thread management
sensor.h
sensor.cpp
analyzer.h
analyzer.cpp
planner.h
planner.cpp
controller.cpp
  src/threads
  src
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 8
Understanding the thread-safety features of MADARA and GAMS
  MADARA was developed with thread-safety in mind
KnowledgeBase
  The KnowledgeBase is a central technology and is inherently thread-safe
  The KnowledgeBase is a collection of key-value data pairs that is protected by recursive mutexes
  Each thread generated by the GPC contains a reference to a KnowledgeBase that is being shared, updated, and read by threads
key1 => value1
key2 => value2
…
  The KnowledgeBase has several thread-safe options of access including simple get/sets, evaluations/waits on KaRL logics, and containers
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 9
Understanding the thread-safety features of MADARA and GAMS
KnowledgeBase
key1 => value1
key2 => value2
key3 => value3
  The preferred way to access the KnowledgeBase from threads is with MADARA containers
  Containers are essentially O(1) constant-time references into the KnowledgeBase
Integer var2
String var3
  Almost all containers are thread-safe
  Only staged containers are non-thread-safe
  Using containers has the following key advantages
    Efficiency of access
    Modifying values with containers does not trigger the network transport but instead aggregates knowledge changes into packets
    Intuitive access design pattern that works well with IDEs and debuggers
Double var1
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 10
Creating a multi-threaded application
  One of the most frequently cited examples of race conditions in multi-threaded applications is in multi-threaded counters
program
thread1
thread2
thread3
  Unprotected counters create race conditions when more than one thread modifies its value
Integer counter
  MADARA containers will prevent such race conditions from occurring because it accesses a KnowledgeBase, which is thread-safe
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 11
Creating a multi-threaded counter (generating files)
  $GAMS_ROOT/scripts/projects/gpc.pl --path $PROJECT_ROOT/counters ---nt thread1 --nt thread2 --nt thread3
Linux terminal
  %GAMS_ROOT%\scripts\projects\gpc.pl --path %PROJECT_ROOT%\counters ---nt thread1 --nt thread2 --nt thread3
Windows: Open Visual Studio Developer Command Prompt (Start->All programs->Visual Studio 20XX->Visual Studio Tools->Developer Command Prompt)
thread1.h
thread1.cpp
thread2.h
thread2.cpp
thread3.h
thread3.cpp
controller.cpp
  src/threads
  src
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 12
Creating a multi-threaded counter (header files)
thread1.h
thread2.h
thread3.h
  src/threads
  Modify each header file to include a madara::knowledge::containers::Integer
#include "madara/knowledge/containers/Integer.h“
  Add the Integer container header file to the includes section at the top of each file
private:
…
madara::knowledge::containers::Integer counter;
  Add a counter to the private section of each thread header file
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 13
Creating a multi-threaded counter (source files)
thread1.cpp
thread2.cpp
thread3.cpp
  Modify each thread cpp file to setup counter and increment it during execution
  Modify the init method to include setting the name of the counter variable
  Modify the run method to increment the count
++counter;
counter.set_name (".counter", knowledge);
  The name of the counter has a period at the front so MADARA treats it as a local variable
    Changes to this variable will not be sent across the network
    If we make this a global variable (no period), then others can change the value
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 14
Creating a multi-threaded counter (modifying controller)
  Modify the controller to set thread hertz rates
  -1 hertz means run once, 0 means as fast as possible, >0 is a specific hertz
  The MADARA Threader provides a scheduling system for predictable thread execution
controller.cpp
  src
// begin thread creation
threader.run (1, "thread1", new threads::thread1());
threader.run (1, "thread2", new threads::thread2());
threader.run (1, "thread3", new threads::thread3());
// end thread creation
  Predictable execution is necessary for verification to be possible
  By providing both thread-safety and predictable execution, you can be more assured of multi-threaded behavior
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 15
Creating a multi-threaded counter (modifying controller)
  In this application, the controller is not needed, so comment out the run method
  Call the MADARA sleep function instead
  The default generation includes a GAMS controller
  GAMS controllers and MADARA threads naturally work together because the KnowledgeBase they depend on is thread-safe
controller.cpp
  src
// controller.run (period, loop_time);
madara::utility::sleep (loop_time);
  This will allow the application to run for a period of time before terminating the threads
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 16
  cd $PROJECT_ROOT/gams_projects/tutorial2
  ./action.sh compile
  bin/custom_controller --loop-time 10
Linux terminal
  cd %PROJECT_ROOT%\gams_projects\tutorial2
  .\action.bat compile
  bin\custom_controller --loop-time 10
Windows: Open Visual Studio Developer Command Prompt (Start->All programs->Visual Studio 20XX->Visual Studio Tools->Developer Command Prompt)
Creating a multi-threaded counter (compile and run the project)
  The custom application will run for 10s and then print out the resulting knowledge
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 17
Understanding networking in MADARA and GAMS
  The GPC generates networking infrastructure for all custom controllers
  All knowledge bases can be connected via one or more multicast, broadcast, unicast or custom transports
KnowledgeBase
key1 => value1
key2 => value2
…
KnowledgeBase
key1 => value1
key2 => value2
…
multicast
broadcast
unicast
  --multicast option passed to controllers specifies a multicast ip and port
  --broadcast option passed to controllers specifies a broadcast ip and port
  Additional transports can be added with the attach_transport function on KnowledgeBase
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 18
Understanding networking in MADARA and GAMS
  Knowledge is sent over the network transports at certain synchronization points
  Evaluate, wait, set, and send_modifieds are synchronization points
  GAMS controller calls send_modifieds at a controllable intervals
KnowledgeBase
key1 => value1
key2 => value2
…
KnowledgeBase
key1 => value1
key2 => value2
…
multicast
broadcast
unicast
  These synchronization points aggregate knowledge into single messages that are applied either all at once or not at all
  As with other timing and control features, the synchronization points combined with thread-safety provide more consistent and predictable execution in distributed systems
  Timing and control are important for verification
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 19
Next steps in this tutorial series
[13:30] Creating distributed algorithms
[14:45] Creating hardware and simulation platforms
Introduction
Generation
Notes
Next Steps
Thread Safety
Example App

## Slide 20
James Edmondson
Email: jredmondson@sei.cmu.edu
U.S. Mail
Software Engineering Institute
4500 Fifth Avenue
Pittsburgh, PA 15213-2612 USA
Website
www.sei.cmu.edu/contact.cfm